11-3           0932347    池宗修

The width of a rectangular slit is measured in the laboratory by means of its diffraction pattern at a distance of 2m from the slit. When illuminated normally with a parallel beam of laser light (632.8nm), the distance between the third minima on either side of the principal maximum is measured. An average of several tries gives 5.625cm.

- Assuming Fraunhofer diffraction, what is the slit width?

- Is the assumption of far-field diffraction justified in this case?What is the ratio L/Lmin?

答:

a.      W=5.625cm/3=1.875cm

=0.135mm

b. Lmin===1.44*10-2

L/Lmin=139