光學作業 應物三甲 0932347 池宗修

Problem 12-2

a. Describe the dispersion in the red wavelength region around 650 nm (both in 0/nm and in nm/mm) for a transmission grating 6 cm wide, containing 3500 grooves/cm, when it is focused in the third-order spectrum on a screen by a lens of focal length 150 cm.

b. Find the resolving power of the grating under these conditions.

ANS：

- a == 2.85*10-4 cm

sin== 0.684

cos== 0.729

D === 14439 rad/cm

D = 14.439*10-4 rad/nm*1800/rad = 0.0827 0/nm

f D = 1500*14.439*10-4 = 2.165 mm/nm

1/2.165 = 0.4618 nm/mm

- N = W/a = 6/2.85*10-4 = 21052

R= mN = 3*21052 = 63256