光學作業 應物三甲 0932372 戴銘昆

Problem 7-18

A soap film is formed using a rectangular wire frame and held in a vertical plane. When illuminated normally by laser light at 632.8 nm, one sees a series of localized interference fringes that measure15 per cm. Explain their formation.

Sol:

因肥皂薄膜在垂直放時,會受重力影響而造成厚度不均勻

已知薄膜干涉的光程差公式:(亮紋位置) 或(暗紋位置)

由於這時兩束相干涉光的光程差只依賴於薄膜的厚度,而由上式可得到干涉條紋所在位置薄膜的厚度為,及兩相鄰亮條紋間對應的厚度差為

設為楔形薄膜的尖劈尖角,則相鄰亮條紋的間距應滿足

sin=/2n,即=

依題目nm ,=1/15(cm) 且設肥皂薄膜的折射率n=1.33

(1/15)*=(632.8*)/(2*1.33*)(=03000356842 (rad)

=

Ans: Soap film becomes wedge-shaped under gravity; the angle of wedge is.