光學作業 應物三甲 0932377 田又仁

Problem 7-23

Newton’s rings are formed between a spherical lens surface and an optical flat. If the tenth bright ring of green light (546.1 nm) is 7.89 mm in diameter , what is the radius of curvature of the lens surface ?

ANS:

由

2nf tm +△r = mλ  bright

已知 △r =λ/2

nf = 1  (in the air) , λ= 546.1 nm , rm = 3.945 mm

所以 => 2nf tm+λ/2= mλ

=>tm = (2m-1)λ/4 -------------(1)

再由 R2 = rm2 + (R-tm)2

=> R= rm2 + tm2 /2 tm --------------(2)

由(1)

tm= (2*10-1)/4 = 19/4*546.1*10-9  = 2.59*10-6

由(2)

所以R =  rm2	 + tm2 /2 tm

= 15.563*10-6+6.7081*10-12/5.18*10-6

= 3m