光學作業 應物三甲 0932385 劉俊緯

OPTICS: Problem 7-27

A laser beam from a 1-mW He-Ne laser (632.8 nm) is directed onto a parallel film with an incident angle of . Assume a beam diameter of 1mm and a film index of 1.414. Determine (a) the amplitude of the E-vector of the incident beam; (b) the angle of refraction of the laser beam into the film; (c) the magnitude of r’ and t t’, using the stoke relation and a reflection coefficient , r = 0.280; (d) the independent amplitude of the first three reflected beam and by comparison with the incident beam, the percentage of radiant power density reflected in each; (e) the same information as in (d) for the first two transmitted beams; (f) the minimum thickness of film that would lead to total cancellation of the reflected beams when they are brought together at a point by a lens.

(a)

=

(b)

- r = 0.28  =  = 0.28

t t’ =   = 0.9216

(d)  = 0.28 * 980 = 274

= 0.9216*0.28*980 = 253

= 0.9216* *980 = 19.8

(e)  = 0.9216*980 =903

= 0.9216**980 = 70.8

(f)

2*1.414 * t *= 632.8nm

t =  = 258nm