光學作業 應物三甲 0932389 王郁雯

Problem 8-3

A thin sheet of fluorite of index 1.434 is inserted normally into one beam of a Michelson interferometer. Using light of wavelength 589 nm , the fringe pattern is found to shift by 35 fringes. What is the thickness of the sheet ?

- m = 2△d /λ = 2(n-1) t /λ

＝＞ 35 × 5.89 × 10-9 = 2 ( 1.434 - 1 ) t

＝＞ t = 23.79 μm