光學作業  應物四 0952178 李晴弘

Problem 8-8

The plates of a Fabry-Perot interferometer have a reflection coefficient of r = 0.99. Calculate the minimum (a) resolving power and (b) plate separation that will accomplish the resolution of the two components of the H-alpha doublet of the hydrogen spectrum, whose separation is 1.360 nm at 656.3 nm.

Sol:

(a)

The resolving power is  48260

(b)

Since the reflection coefficient of r = 0.99

The Finesse   F =  =  = 156.29

And R = 48260 = m F = m*156.29 ( m = 308.785

And m = 308.785 =

( The plate separation d = 1.013* = 0.01013 cm