光學作業  生機3乙 0932530 廖文鏞

Problem 8-9

A Fabry-Perot interferometer is to be used to resolve the mode structure of a He-Ne laser operating at 632.8 nm. The frequency separation between the modes is 150 MHz. The plates are separated by an air gap and have a reflectance () of 0.999

- What is the coefficient of the instrument?

- What is the resolving power required?

- What plate spacing is required?

- What is the free spectral range of the instrument under these conditions?

- What is the minimum resolvable wavelength interval under these conditions?

ANS:

- coefficient of the instrument=coefficient of finesse

formula  F===3.3996×10

b.

formula

Finesse=f==3138.45

FWHM=150MHz========>d=0.318 mm

=3.16×10

c.

FWHM=150MHz========>d=0.318 mm

d.

====>=6.29

e.

=Finesse=3138.45   =====>