光學作業 應物三甲 0932347 池宗修

Problem 8-18

Consider the transmittance of the variable-input-frequency Fabry-Perot cavity shown in figure 8-15. Assume that the Fabry-Perot cavity used has a length of 10cm and that the nominal frequency of the laser input is 4.53*1014 Hz. Find

- The finesse，Ｆ，of the cavity

- The free spectral range，fsr，of the transmittance

- The FWHM，21/2，of a transmittance peak

- The quality factor，Q，of the cavity

- The photon lifetime，p，of the cavity

Ans:

- F==70

- fsr=c/2d=1.5GHz

- 21/2=fsr/F=21MHz

- Q=/21/2=2.2/107

- p=1/   又因=/Q

所以p=8ns