光學作業 應物三甲 0932385 劉俊緯

Problem 10-23

The total delay time due to both modal distortion and material dispersion is given by . Determine the total delay time in a 1-km fiber for which = 1.46, = 1%, = 820 nm, and = 40 nm.

Sol:

=== 48.7 ns

= -M ,   M查表得100 ps/nm-km

= -M= -4 ns

=

= 48.9 ns