10-24

0932386 應物三甲 林慧琪

Waveguide dispersion is measured in a silica fiber at various wavelength using laser diode sources with a spectral width of 2 nm. The results are

| λ(μm) | δ(τ/L)(ps/km) |
| --- | --- |
| 0.70 | 1.88 |
| 0.90 | 5.02 |
| 1.10 | 7.08 |
| 1.40 | 8.40 |
| 1.70 | 8.80 |

- Plot the waveguide parameter M’ versusλ in the range 0.70 to 1.70μm.

- Determine the waveguide dispersion in ps/km at λ = 1.27 and 1.55μm for a source with a spectral width of 1 nm.

Sol:

a.

M’ =δ(τ/L)/Δλ

b.

λ= 1.27

由圖知M’= -3.9 (ps/nm-km)

δ(τ/L) = -M’ Δλ= 3.9 (ps/km)

λ= 1.55，M’=-4.29

δ(τ/L) = -M’ Δλ= 4.29 (ps/km)